46$(h1ii46$)	Cubicle system D-BASIC$(kurz9Partition Wall System Type C$)

Made by KEMMLIT-Bauelemente GmbH
Maltschachstr. 37
72144 Dusslingen

Germany
Telephone: (0049) 7072 / 131-0
Telefax: (0049) 7072 / 131-150
info@kemmlit.de - www.kemmlit.de

Construction:

30 mm thick melamine resin coated particle board.

All visible edges are protected with 3 mm thick

ABS-lipping. The system features a static connection

and vandal-resistant hardware.

TÜV-approved (GS seal of approval).

Options:
Type D-BASIC 1.1: Profiles anodised.
Type D-BASIC 1.2: Profiles powder-coated.

Height:
2000 mm, incl. 150 mm under panel clearance.

As an option also 2135 mm, incl. 150 mm under panel clearance

Partitions and pilasters (front panels):
30 mm thick melamine resin coated particle

board. All visible edges are protected with 3 mm thick

ABS-lipping (2 mm radius) therefore impact- and shatter-

Resistant, reducing the risk of injuries.

Profiles:
All profiles are made of aluminium and rounded (2 mm radius)

to reduce the risk of injuries. Warp-resistant stabiliser

head rail (55/43 mm) placed above the front is oval and

elegantly rounded.

As an option also in a rectangular shape (42/43 mm).

Wall-connection profiles made of U-channels

to allow minor adjustments for tolerances on site.

Supporting legs:

Made of corrosion-free aluminium (Ø 20mm).

Satin anodised or power-coated, with stainless steel

core and stainless steel floor plate. Durable cover sleeve

made of colour-coordinated nylon. Cover sleeve can easily

be lifted for cleaning purposes. Force-fit connection

by means of M12 screw connection to the hinge and

door stop profile.

As an option made entirely of stainless steel (Ø 20 mm).
Continuous height adjustability. Force-fit connection by

means of M12 screw connection to the hinge and door

stop profiles. Stainless steel cover sleeve can easily be

lifted for cleaning purposes.

Doors:
Particle board doors, 30 mm thick, same construction

as partitions and pilasters (front panels).

Doors with blunt door stop, door stop profiles made

of aluminium. To reduce closing noise a rubber profile

seal is integrated in the door stop profile.

Hinges:

2 robust 2-roller-edge hinges (Ø 20 mm) made of

aluminium satin anodised or powder-coated, as an

option made of stainless steel.

As an option 2 robust 2–roller-rising-butt edge hinges

(Ø 20 mm) for self-closing doors made of aluminium,

satin anodised or powder-coated.

Furniture/hardware:

Double latch WC lock. Safety lever handles (Ø 23 mm).

Red/white indicator with emergency release mechanism

made of satin anodised aluminium, stainless steel, or

made of impact and shatter-resistant nylon.

As an option single latch WC lock. Door knobs, red/white

indicator with emergency release mechanism made of

satin anodised aluminium, stainless steel or made of

impact and shatter-resistant nylon.

Colours:
Colours for partitions, pilasters and doors according to

the KEMMLIT colour chart (at least 9 colours).

Profiles, hardware, supporting legs and accessories

available in the same colours according to the KEMMLIT

colour chart (at least 6 colours).

All prices ex works in Dusslingen. Taxes and duties

are unpaid, materials only. Installation and transportation

are not included.$)

$(h1ii46.10$)	$(menge $) 		 0,000 no.          .............$)                   $(gb.............

Accessories for toilet cubicles:

/E

$$NNN

$(h1ii46.20$)	$(menge $)         KEMMLIT door stopper hooks made                     0,000 no.          .............$)                   $(gb.............

of nylon 301      $(d276$)	$(ep$)

$(langAccessories for toilet cubicles $) $)/E

$$NNN

$(h1ii46.30        $)$(langKEMMLIT wall hooks made of nylon 302               0,000 no.          .............$)                   $(gb.............$)

$(menge $)	$(d276$)	$(ep$)

/E

$$NNN

$(h1ii46.40         $)	KEMMLIT paper roll holder made                         0,000 no.           .............$)                  $(gb.............

of nylon 308$(menge $)	$(d276$)	$(ep$)

$(lang$)

/E

$$NNN

$(h1ii46.50$)         KEMMLIT replacement paper roll holder               0,000 no.          .............$)                  $(gb.............

made of nylon 309$(menge$)	$(einh$)	$(d276$)$(ep$)

$(lang$)

/E

$$NNN

$(h1ii46.60$)         $(menge $)KEMMLIT WC-brush set, square-shaped, made   0,000 $)$(einhno.          	.............$)                  $(gb.............$(ep$)

of nylon 310$(d276$)

$(lang$(h1ii

Accessories also available in stainless steel.$)

$)/E$$GRUEnd

----------------------

Cubicle System$(kurz9Partition Wall system Type D-BASIC$)	$(gb.............$)

============

/E